## Slide 1: Implement RANSAC algorithm using Python
Yi Zhao
Mail: zhao.yi@ntnu.no
——Take plane detection as an example
Notes: Hello everyone, my name is Yi Zhao, you can call me Yi. As Prof. Fan introduced the RANSAC algorithm in the previous classes, today I will introduce how to implement the RANSAC using python.

## Slide 2: Steps of implementing RANSAC algorithm using Python
1. Read LAS files
2. Implement RANSAC
3. Evaluate RANSAC results
Notes: In general, it is a three-step work for implementing RANSAC in python, including reading the LAS data, implementing RANSAC, and evaluating the results of the RANSAC

## Slide 3: Steps of implementing RANSAC algorithm using Python
1. Read LAS files using python
  1.1 Load LAS files
  1.2 Clean outlier points (optional)
  1.3 Write new LAS file
Notes: Reading LAS using Python in the first step usually includes three steps loading the file, removing outliers if needed, and writing the remaining points a new file.

## Slide 4: 1. Load LAS files using python
import numpy as np from scipy import stats
import pylas
For LAS data processing
For mathematical operation and statistics
Pip install PackageName
Command for installing the packages
Notes: Before using python to deal with the LAS files, we need to import the necessary packages. Here, we need to import NumPy and stats packages to deal with the mathematical operation and statistics and use the pylas package, which is a python library for reading LAS or LAZ files, to proceeding lidar points.
If you receive an import error like “no module named pylas”, you can use the command: pip install with your package name to install the packages you need.

## Slide 5: 1. Load LAS files using python
#### load by pylas pcd = pylas.read("../Assignment01-Data/Data01.las")
Header (LAS version, point format…)
Variable Length Records (Spatial reference system…)
Point Records (Store the point sequentially)
Function Name
Parameter (the LAS file needs to be loaded)
Variable Name
Notes: Generally, the LAS files are organized in 3 main parts, the header, Variable Length Record, and point records. For the header, it contains information about the data such as LAS data version, the point format (which tells the different dimensions stored for each points). The Variable Length Records are meant to store additional information such as the Spatial Reference System, description on extra dimensions added to the points. And for the point records, it helps to store the points sequentially.
The command for reading LAS by pylas is very simple, using the read function of pylas and fill the parameter with the LAS files’ location and name, the LAS file will be loaded.

## Slide 6: 1. Load LAS files using python
#### create empty LAS file with header new_file = pylas.create_from_header(pcd.header)
Function Name
Parameter (the header of the new LAS file, which is usually the same as the original LAS file)
Variable Name
new_file = pylas.create(point_format_id=2, file_version="1.2")
Notes: When the LAS data was loaded, we need to create an empty LAS file for the processed point cloud data storage. You can use the pylas.create_from_header function to create the empty LAS with the header information, or use the pylas.create function and point format id to create an empty LAS file.

## Slide 7: 1. Load LAS files using python
# find mode for this dataset pcd_z_mode = stats.mode(pcd.z)[0][0] # choose points with z value larger than the mode new_file.points = pcd.points[pcd.z > (pcd_z_mode+2)]
*In statistics, the mode is the value that is repeatedly occurring in a given set.
Parameter (outlier point filter condition )
Notes: Here, we use the mode to filter the outlier points. If the elevation of the point is higher than the mode value of the point dataset over 2 meters, we will assume it is an outlier point and remove it. It should be note that, the filter condition is optional, you need to design the filter condition according to the characters and data distribution of your dataset.

## Slide 8: 1. Load LAS files using python
#### save las file new_file.write("../Assignment01-Data/Data01-cleanheight-1.las")
Function Name
Parameter (the name and path of the new LAS file need to be saved)
Notes: Next, we need to save the remaining points to a LAS file. Similar to the read function, the LAS file write function only needs a parameter that the name and path of the new LAS file need to be saved.

## Slide 9: Steps of implementing RANSAC algorithm using Python
2. Implement RanSAC using python
  1.1 Add random points
  1.2 Calculate plane containing the random points
  1.3 Add points into interior points
  1.4 Save the results
Notes: The second step is to implement RANSAC using python. Following the principles of the RANSAC algorithm, in this step, we need to add random points first and calculate the plane containing the random points, then, add points into interior points according to the selecting condition. Finally, we save the results to a new file.

## Slide 10: 2. Implement RANSAC using python
import numpy as np import pylas import random import math
For mathematical operation and statistics
Add random points for implementing RANSAC
Pip install PackageName
Command for installing the packages
Notes: This is the four packages we need to use, among them, the random package is for adding random points and the math package is for mathematical operation and statistics.

## Slide 11: 2. Implement RANSAC using python
When performing the RANSAC algorithm, the user needs to specify three parameters:
pcd = pylas.read("../Assignment01-Data/Data01.las")
①
Max iterate = 300
②
Distance threshold = 0.15
③
Notes: When performing the RANSAC algorithm for plane , you need to specify three parameters. The first one is the LAS files you are going to deal with. Then is the max iterate number, and the last one is the distance threshold.

## Slide 12: 2. Implement RANSAC using python
# Step 1: add 3 random points
random.seed()
start_points_idx = [random.randint(0, point_count-1) for i_l in range(3)]
print('start_points_idx: ', start_points_idx) p1 = [pcd.x[start_points_idx[0]], pcd.y[start_points_idx[0]], pcd.z[start_points_idx[0]]] p2 = [pcd.x[start_points_idx[1]], pcd.y[start_points_idx[1]], pcd.z[start_points_idx[1]]] p3 = [pcd.x[start_points_idx[2]], pcd.y[start_points_idx[2]], pcd.z[start_points_idx[2]]]
Assign the coordinates of the searched point to p1
Search three different seed points for implementing RANSAC
Returns an integer within the start and end range
random.randint(start, end)
Iterate three times to determine three seed points
p1
p2
p3
Notes: To implement the RANSAC method for plane detection, we need to determine an initial plane first.
Mathematically, to determine a plane, we need three points that are not on the same line. Here, we use random.seed() function to determine three different integers, and use the three integers as the indexes of the points to search three points with different coordinates. It should be noted that the three integers are generated by the random.randint() function with FOR loop, the function of the random.seed() is to make sure the three integers are not the same.
As shown in the figure, through this process, three different points are randomly selected, they are point one, two and three.

## Slide 13: 2. Implement RANSAC using python
# Step 2: Calculate plane contains p1, p2 and p3 # Plane equation: ax + by + cz + d = 0 # p1: x1, y1, z1 # p2: x2, y2, z2 # p3: x3, y3, z3 a = (p2[1] - p1[1]) * (p3[2] - p1[2]) - (p2[2] - p1[2]) * (p3[1] - p1[1]) b = (p2[2] - p1[2]) * (p3[0] - p1[0]) - (p2[0] - p1[0]) * (p3[2] - p1[2])
c = (p2[0] - p1[0]) * (p3[1] - p1[1]) - (p2[1] - p1[1]) * (p3[0] - p1[0])
d = -(a * p1[0] + b * p1[1] + c * p1[2])
p1 (x1, y1, z1)
p2 (x2, y2, z2)
p3 (x3, y3, z3)
Plane
Notes: Here, we calculate the plane function according to the three seed points. Mathematically, a plane equation is defined as ax + by + cz + d = 0, since we already have the coordinates of three points, we bring them into the calculation equation of the plane, then the coefficients a, b, c, and d in the equation can be expressed as above by the coordinates of these three points.
As shown in this figure, the red triangle is the plane determined by the three random points.

## Slide 14: 2. Implement RANSAC using python
# Step 3: add points into interior points # Skip points have be chosen as seed # pcd_p_search = np.delete(self.pcd_p, start_points_idx, axis=0) # Calculate distance between the point and the plane # (now all point are in calculating, including 3 samples)
plane_len = max(0.1, math.sqrt(a*a + b*b + c*c)) dist = np.abs((a*pcd_p[:, 0] + b * pcd_p[:, 1] + c * pcd_p[:, 2] +d)) / plane_len
Notes: As the initial plane has been determined, next, we need to search the interior points belonging to this plane according to the distance threshold we set. Therefore, we need to calculate the distance of every point to the initial plane. The distance calculation equation is shown in white bold font on the right.

## Slide 15: 2. Implement RANSAC using python
# Add points in distance threshold as interior points interior_idx = np.where((dist <= thres_dis))[0] print(interior_idx.shape) pcd_p_interior = pcd_p[interior_idx, :]
Condition of selecting interior points
Add sleeted points to plane according to its index
Plane
Distance
Notes: As long as the distance of the point to the plane is less than the threshold we set, we assume it is an interior point, and added it to the interior point dataset according to its index.

## Slide 16: 2. Implement RANSAC using python
# update the best model if (pcd_p_interior.shape[0] > best_interior.shape[0]) and (pcd_p_interior.shape[0]< point_count): print('updating...’)
best_interior = pcd_p_interior best_interior_idx = interior_idx best_plane = [a, b, c, d, plane_len] pcd.classification[interior_idx] = pcd.classification[interior_idx] + class_number
Conditions for updating the “best” plane
Using current information, such as the number of the interior points, the plane equation
New Plane
Notes: In this step, we need to find or update the “best” plane. If there are enough inlier points, and the point number included in the new plane is more than the original “best” plane, the plane from this iteration will be set as the new “best” plane. Repeat the previous steps, until the iteration number is equal to the maximum iteration number.

## Slide 17: 2. Implement RANSAC using python
# save result new_file = pylas.create_from_header(pcd.header) new_file.points = pcd.points[best_interior_idx] new_file.write(“…\code-assignment01\Assignment01-Data/B1_{}.las".format(i))
Notes: After the whole RANSAC process, most points can be grouped into a plane. And the plane detection is completed. Now we use the pylas create and pylas write function to save the results.

## Slide 18: END
Notes: This is all the content we introduced in this class, now is your time, you can train your code on your PC and if you have question we can discuss. Next time, that is tomorrow, we will introduce how to evaluate the RANSAC results.